## Slide 1: Diode Circuit Problems & Logic Gates
Course No: CSE 251
Course Title: Electronic Devices and Circuits
Lecture 9
Partial Credit:
Aroni Ghosh (AGS)
Lecturer(On Leave), CSE, Brac University

## Slide 2: Problem 2(Use CVD model)

## Slide 3: Problem 3(Use Ideal model)

## Slide 4: Problem 4(CVD model)
Ans: Vo=6.865 V

## Slide 5: Problem 5(CVD model)
Ans: Vo=2V

## Slide 6: Logical Operations with Diode (OR)
Logic Truth Table
Voltage Truth Table
Low/False High/True
Logic Levels: 0 1
Corresponding voltage levels: 0V 5V

## Slide 7: Logical Operations with Diode (OR)
Case 1: VA= 0V, VB= 0V
Both D1 and D2 are off as Vanode<Vcathode
Replace D1 and D2 with open circuits.
So, VC= 0V
D1
D2
R is a Pull Down Resistor which pulls down the voltage of VC from floating condition to 0V.

## Slide 8: Logical Operations with Diode (OR)
Case 2: VA= 0V, VB= 5V
D1 is off and D2 is on
Replace D1 with open circuit and D2 with short circuit.
So, VC= VB= 5V
Case 3: VA= 5V, VB= 0V
D1 is on and D2 is off
Replace D1 with short circuit and D2 with open circuit.
So, VC= VA= 5V
Case 1: VA= 5V, VB= 5V
Both D1 and D2 are on
Replace D1 and D2 with short circuits.
So, VC= VA= VB= 5V

## Slide 9: Logical Operations with Diode (AND)
Logic Truth Table
Voltage Truth Table

## Slide 10: Logical Operations with Diode (AND)
Case 1: VA= 0V, VB= 0V
Both D1 and D2 are on as Vanode>Vcathode
Replace D1 and D2 with short circuits.
So, , VC= VA= VB= 0V
D1
D2
R is a Pull Up Resistor which pulls up the voltage of VC from floating condition to 5V.

## Slide 11: Logical Operations with Diode (AND)
Case 2: VA= 0V, VB= 5V
D1 is on and D2 is off
Replace D1 with short circuit and D2 with open circuit.
So, VC= VA= 0V
Case 3: VA= 5V, VB= 0V
D1 is off and D2 is on
Replace D1 with open circuit and D2 with short circuit.
So, VC= VB= 0V
Case 1: VA= 5V, VB= 5V
Both D1 and D2 are off
Replace D1 and D2 with open circuits.
So, VC= 5V

## Slide 12: Effect of input Voltage Variation in Logic Gates (OR)
D1
D2
Case 1: Assuming both D1 and D2 are on
Replace D1 and D2 with short circuits.
So, VC is short with both VA and VB
Can VC be 4V and 5V at the same time???
So this assumption is wrong!
If VA= 4V and VB= 5V, what is the value of output VC?

## Slide 13: Effect of input Voltage Variation in Logic Gates (OR)
Case 2: Assuming both D1 and D2 are off
Replace D1 and D2 with open circuits. So, VC= 0V
But now Vanode(4V for D1, 5V for D2)>Vcathode(0V) for both diode
So this assumption is also wrong!
Case 3: Assuming D1 is on and D2 is off
Replace D1 with short circuit and D2 with open circuit. So, VC= VA= 4V
But now for D2, Vanode(5V)>Vcathode(4V). So, D1 should have been ON!
So this assumption is also wrong!
Case 4: Assuming D1 is off and D2 is on
Replace D1 with open circuit and D2 with short circuit. So, VC= VB= 5V
Now for D1, Vanode(4V)<Vcathode(5V). So, D1 should be OFF!
So this assumption is correct!

## Slide 14: Effect of input Voltage Variation in Logic Gates (OR)
Example 4: Find the value of Vo
D1 and D2 are OFF  Open Circuit
Only D3 is ON  Short Circuit
Vo= 4.5V
Current, I= 4.5V/2k= 2.25 mA

## Slide 15: Effect of input Voltage Variation in Logic Gates (AND)
Case 1: Assuming both D1 and D2 are on
Replace D1 and D2 with short circuits.
So, VC is short with both VA and VB
Can VC be 1V and 2V at the same time???
So this assumption is wrong!
If VA= 1V and VB= 2V, what is the value of output VC?

## Slide 16: Effect of input Voltage Variation in Logic Gates (AND)
Case 2: Assuming both D1 and D2 are off
Replace D1 and D2 with open circuits. So, VC= 5V
But now Vanode(5V)>Vcathode(1V for D1 & 2V for D2) for both diode
So this assumption is also wrong!
Case 4: Assuming D1 is on and D2 is off
Replace D1 with short circuit and D2 with open circuit. So, VC= VA= 1V
Now for D2, Vanode(1V)<Vcathode(2V). So, D2 should be OFF!
So this assumption is correct!
Case 3: Assuming D1 is off and D2 is on
Replace D1 with open circuit and D2 with short circuit. So, VC= VB= 2V
But now for D1, Vanode(2V)>Vcathode(1V). So, D1 should have been ON!
So this assumption is also wrong!

## Slide 17: Effect of input Voltage Variation in Logic Gates (AND)
Example 5: Find the value of Vo
D1 and D2 are OFF  Open Circuit
Only D3 is ON  Short Circuit
Vo= -5V
= 5 mA

## Slide 18: Thank You