## Slide 1: CSE251: Electronic Devices and Circuits
Credit:
Shadman Shahid (SHD)
Lecturer, Department of Computer Science and Engineering, School of Data and Sciences, BRAC University
Email: ext.shadman.shahid@bracu.ac.bd
Lecture: MOSFET

## Slide 2: Transistors as Digital Switch
Transistors are 3 terminal non-linear devices, can be used as switch
2 types – Voltage Controlled, Current Controlled
Metal Oxide Semiconductor Field Effect Transistor (MOSFET) are voltage controlled
Control, . The IV characteristics ( vs ) depends on
Actual dependency is complex.
Will start with a simple (but approximate) one – S-Model (Switch Model)

## Slide 3: MOSFET S-Model
The MOSFET (approximately) behaves like a switch
. Here, , and

## Slide 4: MOSFET S-Model

## Slide 5: Logic Gates using MOSFET
Just replace the switches with MOSFETs!
NOT Gate (Inverter)
NAND Gate (Inverter)
NOR Gate (Inverter)

## Slide 6: MOSFET Logic Gates – More Examples
𝑂𝑈𝑇 = 𝐴𝐵 + 𝐶 + 𝐷
𝑂𝑢𝑡 =
𝐴 + 𝐵 𝐶𝐷 =
𝐴 + 𝐵 𝐶𝐷
Vs
Vs
Vs

## Slide 7: Practice Problem
Design a circuit using ideal MOSFETs (S-model) to implement the logic function
[De Morgan’s Theorem]

## Slide 8: Voltage Transfer Characteristics (VTC)
Reminder: VTC is a graph where axis = input voltage, -axis = output voltage
When (Logical 0) (Logical 1)
When (Logical 1) (Logical 0)

## Slide 9: VTC of NAND gate
When
When
We only have one axis, but two inputs
Solution: Draw two VTC, one considering one considering

## Slide 10: VTC of NAND gate
𝑉Y = 0
𝑉Y = 1
Homework: Find VTC for NOR gate
When
When
We only have one axis, but two inputs
Solution: Draw two VTC, one considering one considering

## Slide 11: Outline
Constructing a *real* MOSFET – n/p-channel
Operation of an MOSFET-
  Cut-Off
  Saturation
  Triode Mode
Output Characteristics
PWL Model and Non-ideal Analysis: SR model**
Real MOSFET equations
**Probably won’t cover

## Slide 12: Construction of Real MOSFET
100
𝜇𝑚
Top view of several n-channel MOSFETs fabricated on a chip. The square MOSFETs in the center of the photograph have a width and length of 100 μm. (Photograph Courtesy of Maxim Integrated Products.)

## Slide 13: Real MOSFET – Enhancement Type
Device Structure (n-channel MOSFET)

## Slide 14: n-channel MOSFET (NMOS) Physical Structure
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
e
e
e
e
e
e
h
h
h
h
h
h
Enhancement Type

## Slide 15: NMOS in Equilibrium
When the transistor is left alone, some electrons from the n-type wells diffuse into the p-type material to fill holes.
This creates negative ions in the p-type material and positive ions are left behind in the n-type material.
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
+
+
+
+
+
+
_
_
_
_
_
_
h
h
h
h

## Slide 16: NMOS in Cutoff
When a small, positive VGS is applied, holes “move away” from the gate.
Electrons from complete atoms elsewhere in the p-type material move to fill holes near the gate instead.
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
+
+
+
+
+
+
_
_
_
_
_
_
h
h
h
h
-
+
_
_
_
h
VGS > 0

## Slide 17: NMOS Transistor channel
When VGS is larger than a threshold voltage VTH(n), the attraction to the gate is so great that free electrons collect there.
The applied VGS creates an induced n-type channel under the gate (an area with free electrons).
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
+
+
+
+
+
+
_
_
_
_
_
_
h
h
h
h
-
+
_
_
_
h
VGS > VTH(n)
h
h
h
h
h
e
e
e
e
e

## Slide 18: NMOS Transistor Drain Current
When a positive VDS is applied, the free electrons flow from the source to the drain. (Positive current flows from drain to source).
The amount of current depends on VDS, as well as the number of electrons in the channel, channel dimensions, and material.
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
+
+
+
+
+
+
_
_
_
_
_
h
h
h
h
-
+
h
VGS > VTH(n)
h
h
h
h
h
-
+
VDS > 0
_
_
_
_
e
e
e
e
e

## Slide 19: NMOS Transistor Circuit symbol
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
-
+
VGS
-
+
VDS
ID
IG
G
D
S
ID
IG
- VDS +
+
VGS
_

## Slide 20: NMOS I-V Characteristic
G
D
S
ID
IG
- VDS +
+
VGS
_
Since the transistor is a 3-terminal device, there is no single I-V characteristic.
Note that because of the insulator, IG = 0 A.
We typically define the MOS I-V characteristic as
ID vs. VDS for a fixed VGS.
The I-V characteristic changes as VGS changes.

## Slide 21: Modes of Operation
For small values of VGS, VGS ≤ VTH(n), the n-type channel is not formed. No current flows. This is cutoff mode.
When VGS > VTH(n), current ID may flow from drain to source, and the following modes of current flow are possible.
  The mode of current flow depends on the propelling voltage, VDS, and the channel-inducing voltage,
  VGS – VTH(n).
  When VDS < VGS – VTH(n), current is starting to flow. ID increases rapidly with increased VDS. This is triode mode.
  When VDS ≥ VGS – VTH(n), current is reaching its maximum value. ID does not increase much with increased VDS. This is called saturation mode.

## Slide 22: Water Tap Analogy
Imagine the water tap on your kitchen sink.
To make water flow, the water supply has to be connected to the water tap. This establishes a path for water to flow.
Setting VGS above the threshold voltage is like connecting the water supply.
Cutoff = water supply disconnected (no path for current flow)
Setting VGS to a larger value is like connecting a high-pressure water supply—more flow can potentially occur.

## Slide 23: Water Tap Analogy
 | MOSFET Schematic |  | Water Tap

## Slide 24: Water Tap Analogy
The water tap itself is used to adjust water flow. You can turn the flow up and down.
VDS is like the water tap. It controls the amount of flow.
There is, of course, a saturation point. If you keep turning the water tap control, eventually you won’t get any more flow.
Triode = water tap in “normal range”, controls flow
Saturation = water tap turned up to (or past) point for maximum flow

## Slide 25: Water Tap Analogy

## Slide 26: Water Tap Analogy

## Slide 27: Water Tap Analogy

## Slide 28: NMOS Equations
Cutoff Mode
Occurs when
Triode Mode
Occurs when and
Saturation Mode
Occurs when and
: Overdrive Voltage
The minimum voltage necessary at the gate terminal to form a channel.
Indicates the available excess voltage at gate after forming the n-channel.

## Slide 29: Solving Circuits with MOSFET
Use Method of Assumed State!
Three steps:
  Assume: One of the modes (Cutoff, Triode, Saturation)
  Solve: Use corresponding equation and KCL+KVL
  Verify: Check if the conditions of and are satisfied. If not, repeat.
Might need to solve quadratic equation (𝑎𝑥2 + 𝑏𝑥 + 𝑐 = 0).
If we get two roots, choose the one that’s favorable to your assumption

## Slide 30: Example 1
Analyze the circuit to find and using the Method of Assumed State. Here, the input of the MOSFET is . You must validate your assumptions.
Assume:
  Let MOSFET be in Saturation mode:
  or
Solve:
Current Equation:
Verify: For Saturation mode
But here,
Here, the conditions are NOT fulfilled.
Assumption is INCORRECT!

## Slide 31: Example 1
Analyze the circuit to find and using the Method of Assumed State. Here, the input of the MOSFET is . You must validate your assumptions.
MOSFET is in Triode Mode.
or

## Slide 32: Example 2
Design the circuit, that is, determine the values of and , so that the transistor operates at and . The NMOS transistor has , .
Assume:
  Let MOSFET be in Saturation mode:
Solve:
Current Equation:
or

## Slide 33: Example 2
Design the circuit, that is, determine the values of and , so that the transistor operates at and . The NMOS transistor has , .
Verify:
Clearly
Assumption is CORRECT!

## Slide 34: Example - 3
For the circuit, find the value of that results in . The MOSFET has , ,
Assume:
  Let MOSFET be IS in Saturation mode:
Proof:
  Saturation Mode
Solve:
Current Equation:

## Slide 35: Example - 4

## Slide 36: Example - 4
Assume:
  Let MOSFET be in Saturation mode:
Solve:
Current Equation:
or

## Slide 37: Example - 4
Verify:
For Saturation mode
Assumption is CORRECT!

## Slide 38
Example - 5
Solve:
  Both MOSFET are in SATURATION:
  Q1:
  Q2:
Current Equation:

## Slide 39
Example - 5
Solve:
or

## Slide 40: NMOS I-V Characteristic
vs
When :
  for any

## Slide 41: NMOS I-V Characteristic
triode mode
cutoff mode (when VGS < VTH(N))
saturation mode
VDS
ID
VGS = 3 V
VGS = 2 V
VGS = 1 V
VDS = VGS - VT

## Slide 42: n-channel MOSFET - Summary
G – Gate: Trigger terminal
S – Source: Charge carrier reservoir
D – Drain: Charge carrier sink
No channel, open ckt
The created channel will have some R
-> SR model
Small Triode Mode
Large Saturation Mode
Cut off mode

## Slide 43: n-channel MOSFET - Summary
SR model is a better approximation than S model.
Triode Mode exists until: <=
Indicates the available excess voltage at gate after forming the n-channel.
SR Model:

## Slide 44: Review – MOSFET
Control controls the IV between drain-source ( vs )
Threshold voltage = 𝑉T, minimum voltage required to create the channel
Models
S Mode: Assumes an ideal channel with zero resistance
SR Model: Assumes finite channel resistance, depends on

## Slide 45: IV Characteristics of Real MOSFET
Mode | Condition | Equation
Cutoff | 𝑉%& < 𝑉' | 𝐼) = 0
Triode | 𝑉%& ≥ 𝑉' 𝑉)& < 𝑉!( | 𝐼 = 𝑘[𝑉 𝑉 − 1 𝑉* ] ) !( )& 2 )&
Saturation | 𝑉%& ≥ 𝑉' 𝑉)& ≥ 𝑉!( | 𝐼 = 𝑘 𝑉* ) 2 !(